## Slide 1
PHARMACEUTICAL QMS
Quality Management
System Workflows
A Real-World Walk-Through: Metformin HCl (API) → Glucophage® 500 mg Tablet (FDF)
Deviations · CAPA · Quality Checks · Change Control · Recalls
Deviation Mgmt
CAPA
QC Testing
Change Control
Product Recall
AIVOA.AI | Pharmaceutical & Life Sciences

## Slide 2
WHAT IS A QMS — AND WHY DOES IT MATTER?
Quality Management System
A structured set of processes, procedures, and responsibilities that ensure pharmaceutical products meet regulatory and safety standards.
Mandated by FDA 21 CFR Part 211, ICH Q10, and EU GMP guidelines.
Covers the FULL product lifecycle—from raw material sourcing to patient delivery.
Our Case Study
API
Metformin Hydrochloride
Active Pharmaceutical Ingredient
Antidiabetic · biguanide class · widely manufactured globally
↓ processed into
FDF
Glucophage® 500 mg Tablet
Finished Dosage Form
Film-coated oral tablet · sold in 100+ countries
Regulatory Framework: FDA 21 CFR Part 211 | EU GMP Annex 15 | ICH Q10

## Slide 3
QMS MODULE MAP — Key Systems in Daily Operations
Deviation
Management
Capture & assess unexpected events during manufacturing
CAPA
Corrective & Preventive Actions to eliminate root causes
Change
Control
Manage & document approved changes to processes/materials
Complaints
& Recalls
Handle adverse events; initiate product recalls if needed
QC Testing
& Release
Analytical tests on API & FDF batches before release
Document
Control
Version-controlled SOPs, batch records, specifications
Supplier
Qualification
Audit & qualify API suppliers (e.g. Metformin HCl source)
All modules feed into a centralised electronic Quality Record System (eQMS)
Interconnected lifecycle coverage
▶ We will now trace a realistic scenario through four of these modules.

## Slide 4
THE PRODUCT LIFECYCLE & QMS TOUCHPOINTS
Metformin HCl API → Glucophage® 500 mg Tablet
1
Supplier
Qualification
Supplier Audit
Qualification Report
2
API Receipt
& Testing
CoA Review
QC Incoming Inspection
3
Manufacturing
& Blending
Batch Record
Deviation Capture
4
Tablet
Compression
In-Process Checks
Wt/Hardness/Thickness
5
QC Release
Testing
HPLC Assay
Disso / Sterility
6
Distribution
& PV
Complaints Handling
Recall Readiness
QMS ensures every stage is documented, tested, and traceable — from raw API to patient.
Next: Four detailed module scenarios →

## Slide 5
MODULE 1
Deviation Management
⚠ REAL SCENARIO: During tablet compression of Glucophage® Batch GX-2024-117, the in-process check records a mean tablet weight of 498 mg — below the 500 ± 3 mg specification. The operator flags this immediately.
1
Detection & Reporting
Operator documents the weight OOS event in the Batch Manufacturing Record (BMR) and raises a Deviation Report in the eQMS within 1 hour.
2
Initial Assessment
QA reviews severity: Is this a 'minor', 'major', or 'critical' deviation? Tablet weight OOS = Major deviation. Batch GX-2024-117 is placed on hold.
3
Root Cause Investigation
Investigation team checks: Metformin HCl moisture content (API), blend uniformity, compression force settings, and die/punch wear.
4
Impact Assessment
Determine if adjacent batches (GX-2024-115, 116) are affected. Review API CoA from supplier for variability.
5
Disposition Decision
Root cause found: worn punch → batch rejected; press repaired; CAPA initiated. Regulatory notification assessed per jurisdiction.

## Slide 6
MODULE 2
CAPA — Corrective & Preventive Action
Triggered by the Deviation above (worn punch → weight OOS). CAPA-2024-042 is opened to prevent recurrence across all tablet compression lines.
CORRECTIVE ACTIONS (fix the known problem)
Reject Batch GX-2024-117; quarantine & destroy per SOP-DISP-003
Replace worn punch set on Compression Press #3
Verify adjacent batches GX-2024-115 & 116 — release or reject
Regulatory disclosure to FDA if mandatory threshold met
PREVENTIVE ACTIONS (stop recurrence)
Revise Preventive Maintenance SOP: punch/die inspection every 500k units
Add automated in-process weight monitoring (PAT system) on all presses
Update supplier qualification: tighter Metformin moisture spec ≤ 0.3%
Train all compression operators on early OOS detection — re-qualification
Schedule 30-day CAPA effectiveness check with QA sign-off
CAPA must be closed with documented evidence before the next manufacturing campaign.

## Slide 7
MODULE 3
QC Testing & Batch Release
API INCOMING TESTS — Metformin HCl
Identity (IR Spectroscopy)
Matches reference spectrum
✓ PASS
Assay (HPLC)
≥ 99.0% on dried basis
✓ PASS
Related Substances
Total impurities ≤ 0.5%
✓ PASS
Residual Solvents (GC)
ICH Q3C limits
✓ PASS
Moisture Content (KF)
≤ 0.5%
✓ PASS
Particle Size (Laser diffraction)
D90 ≤ 150 µm
✓ PASS
Microbial Limits
TAMC ≤ 1000 CFU/g
✓ PASS
FDF RELEASE TESTS — Glucophage® 500 mg
Description (visual)
White oval film-coated tablet
✓ PASS
Identification (UV/HPLC)
Matches Metformin standard
✓ PASS
Assay (HPLC)
95.0–105.0% of stated 500 mg
✓ PASS
Dissolution (USP App II)
≥ 80% in 30 min at pH 6.8
✓ PASS
Content Uniformity
RSD ≤ 6%, no unit <75% or >125%
✓ PASS
Hardness / Friability
80–120 N / Friability ≤ 1%
✓ PASS
Disintegration
≤ 45 min
✓ PASS
Microbial Limits
TAMC ≤ 1000 CFU/g, yeast ≤ 100
✓ PASS
All tests passing → QP (Qualified Person) signs the batch release record → Product released to distribution.

## Slide 8
MODULE 4
Complaint Handling & Product Recall
⚠ NEW SCENARIO: 6 months post-release, 14 pharmacies report that Glucophage® 500 mg tablets are splitting in blister packs. Post-market surveillance flags this as a potential product quality complaint requiring recall assessment.
1. Complaint
Receipt
Pharmacies report via product surveillance hotline. All 14 reports logged in eQMS. Batch numbers recorded: GX-2024-118 to 122.
2. Initial
Investigation
Recall coordinator pulls batch records, checks dissolution & hardness data. QC confirms tablets below hardness spec in retained samples.
3. Recall
Decision
Risk Assessment: hardness failure → tablets may fail to disintegrate → dosing issue. Decision: Class II Voluntary Recall (FDA classification).
4. Notify &
Retrieve
Notify FDA within 3 days. Alert distribution chain (wholesalers → pharmacies). Issue Urgent Drug Recall notices. Collect returned stock.
5. Effectiveness
Check
Audit retrieval completeness: ≥ 90% recovery required. Initiate CAPA on hardness specification. Prepare regulatory submission.
Recall completeness must be verified. Root cause feeds back into CAPA and Change Control for permanent fix.

## Slide 9
HOW THE QMS MODULES CONNECT
An event in one module automatically triggers action in others — this is what makes QMS a system, not just a checklist.
eQMS
Database
Deviation
Mgmt
CAPA
Change
Control
QC Testing
Recalls
Doc
Control
When a Deviation is raised → CAPA is triggered → Change Control documents the fix → QC re-tests → Recall prevented.

## Slide 10
KEY TAKEAWAYS
Why QMS is the Backbone of Pharmaceutical Manufacturing
🔬
Every batch is traceable
From the Metformin HCl Certificate of Analysis to the final Glucophage® tablet, the full chain of custody is documented in the QMS.
⚡
Problems trigger automatic workflows
A tablet weight OOS automatically opens a Deviation → CAPA → Change Control sequence. Nothing falls through the cracks.
🛡️
Regulatory compliance is built-in
All actions, approvals, and evidence are time-stamped and auditable for FDA inspections and EU GMP compliance.
🔄
Continuous improvement loop
CAPA effectiveness checks and Post-Market Surveillance feed back into manufacturing processes — the system learns.
AIVOA.AI builds intelligent software that digitises and automates exactly these QMS workflows — turning paper-based pharmaceutical processes into real-time, AI-powered quality operations.